## Slide 1
Bike Works Learning
Robotics Otto Build
Uzma Nishat
Ben Loftin
6/7/2019

## Slide 2: BikeWorks Robotics Otto Build

## Slide 3: Introduction
Build Preparations
  Need small screwdrivers for the servo horn screws
    Should order 4 of these magnetized screw drivers, will be good for any kit too
      https://www.amazon.com/ORIA-Screwdriver-Professional-Precision-Smartphone/dp/B01E16J6RQ/ref=sr_1_8?keywords=JIS+%23000&qid=1556738854&s=gateway&sr=8-8
  Need to install the CH341SER driver since the kit comes with the Arduino nano knockoff, it is a Chinese manufacture so only to be installed on personal computers
    Linux laptops/computers have the driver already installed
  Otto DIY code, 3D printed parts and instructions are on github
    https://github.com/OttoDIY/DIY
  Kit is missing servo horn screws needed (8mm servo horn screw)
    maybe hard to tell screw size but these can be extra motors too
      https://www.amazon.com/Longruner-Helicopter-Airplane-Controls-KY66-5/dp/B01NA80LUR/ref=sr_1_8?keywords=9g%2Bservo&qid=1556738416&s=gateway&sr=8-8&th=1

## Slide 4: Otto DIY Interactive Robot
Arduino Nano controlling servo motors and detecting distance with sonar sensor

## Slide 5: Sonar Sensor
Ultrasonic sensor that measures distance by using ultrasonic waves
T: Time from emission to reception
C: Speed of ultrasonic wave

## Slide 6: Otto Step 1
Push motor all the way through to poke out other side
Be careful not to strip screws
  Use the longer servo screws (8 mm)
Don’t overtighten, plastic breaks easily

## Slide 7: Otto Step 2
Double check the movement of motors by hand
  Needs to be able to go close to 180 degrees
  If not done right you will have to reassemble later
Put on safety glasses to cut, flying plastic!
Cut shorter
Note orientation of both parts
Smaller screw

## Slide 8: Otto Step 3
Double check the movement of motors by hand
  Needs to be able to go close to 180 degrees
  If not done right you will have to reassemble later
Plastic bag hack might not be best in long run
Put wires in first
Roll up one of the small plastic bags and stuff on this side to hold in motor better

## Slide 9: Otto Step 4a
M2 bolt would be better than using the servo horn screws
  Need 2 M2x 10mm bolts and nuts per kit
For M2 bolt screw all the way in first before nut
Replace with M2 x 10mm bolt and nut for more secure attachment than long servo screw
Do for both legs
Use tweezers for nut

## Slide 10: Otto Step 4b
Easy step but be gentle and go in at angle
Note that the weight of robot holds the feet in place
  Would be good with a dab of hot glue to hold in
Flat part of feet face outward on both sides
Front
Feet Orientation

## Slide 11: Otto Step 5
Make sure the motors rotate within the limits

## Slide 12: Otto Step 6a
Firmly but gently put the nano into the shield
  Make sure pins are pushed all the way flushed
Check for bent pins before inserting!
USB and power plug on same side
All the way flush

## Slide 13: Otto Step 6b
Install Sonar module before Arduino Nano into ‘head’
Must be done before Arduino board in step 7
Note Pin orientation

## Slide 14: Otto Step 7
Check ground brown wire goes to G pin
It is worth running a test program on motors
Note Pin numbers and orientation

## Slide 15: Otto Step 8a
Important to cut out bigger power plug opening
Sonar module must be installed first
Cut out more with wire cutters and/or chisel tool

## Slide 16: Otto Step 8b
Kits are short a screw so only use one here
One screw only!

## Slide 17: Otto Step 9a
Connect Battery holder to switch
  Plug in 2 pin header into red/black battery pack connector
  Optionally: One can remove red wire/strip some insulation and twist wires together to make connection (use tape to insulate)
Allow students to come up with their own solutions

## Slide 18: Otto Step 9b
Prepare battery/switch wire wrap wire
  Watch video - https://www.youtube.com/watch?v=8SSOKppwpAE
  Strip the wire on both ends, about an inch
Allow students to come up with their own solutions
Stripper tool is inside wire wrap tool
wire wrap tool

## Slide 19: Otto Step 9c
Prepare battery/switch wire wrap wire
  Strip the wire on both ends, about an inch
Keep bare wires nice and striaght
Stripper tool is inside wire wrap tool
wire wrap tool
1 inch off

## Slide 20: Otto Step 9d
Wrap wire onto battery red wire header
  There are 2 holes on end of wire wrap tool, wire goes in top and along channel while the post to wrap onto goes into the center hole
  ** note bare wire is entirely through tool hole up to insulation
It is strange your first time…
Wire through top hole and into channel
Header post into center hole

## Slide 21: Otto Step 9e
Gently twirl the tool and slowly lift tool away
When all wire is wrapped push tool all the way in to scrunch the wire nicely as in picture
Clean connection is what you want

## Slide 22: Otto Step 9f
Repeat attaching other end to switch
Ohm out the switch as exercise in connectivity
The two outside post an a single side is what you will be connecting too

## Slide 23: Otto Step 9g
Repeat attaching other end to Pin 11 V on the nano board
V is Vin, middle row of posts

## Slide 24: Otto Step 9h
Wire wrap is finished showing switch in series

## Slide 25: Otto Step 9i
Use female to female cables provided to attach battery ground (black wire) to nano board ground, pin 11 G
G is Ground, outside row of posts
Attach Grey wire to black
Pin 11, G for ground row

## Slide 26: Otto Step 9j
Tape the open metal on the battery connector with electrical or blue masking tape to keep insulated
Optionally: At home connect wires via wire splicing
  https://www.youtube.com/watch?v=O-ymw7d_nYo
Feel free to do wire splice at home to improve

## Slide 27: Otto Step 9k
Put piezo speaker and switch into the base
If too tight of fit, scrape plastic on robot
Holds Switch in place

## Slide 28: Otto Step 10
Connect Piezo speaker to Pins 13
  (+) on speaker goes to Pin 13 S
  Other speaker pin to Pin 13 G
Connect Sonar to Pins 8/9
  Note Echo and Trigger pins can be swapped, easy change in code
Some Sonars have echo/trigger swapped
Don’t do this we are connected to Pin 11

## Slide 29: Otto Step 11
Place battery pack (with batteries) into base
  Note you may want to test your spread before final assembly
Good idea to test some code before assembly

## Slide 30: Otto Step 12
Put top/head on and program away!
Good idea to test some code before assembly

## Slide 31: Otto Programming Setup
Copy RobotClass\DIY\libraries folder into MyDocuments\Arduino\libraries
Copy Otto Libraries before compiling Otto examples

## Slide 32: Otto Programming Music
Code examples under RobotClass\DIY
Start with playing music
  Otto_MarioBros
  Otto_jingle
  Otto_happybirthday
Try making your own music!

## Slide 33: Otto Programming Movement
Code examples under RobotClass\DIY
Start with these
  Otto_avoid_mhs
  Otto_smooth_criminal_US
  Otto_singleladies
Can you make your own movements?